COMPONENT LIBRARY FOR ANDROID APPLICATION DEVELOPMENT

Component is a user interface builder library that eliminates the tedious works involved in building UI components programmatically and the need to think about developing for different screen sizes and screen densities.

Using Component library, UI components can completely and easily be built programmatically without using layout resources (xml). Though you can use layout resources (xml) alongside building components programmatically using Component library, but it's not necessary. Sticking to building UI components programmatically using Component library alone will help simplify your work.

Component is primarily based on the formula below, which is enclosed in a utility method named ‘dimen’:

dimension = pixel * (densityDPI / DENSITY_DEFAULT)

Where,

pixel = value you give to the ‘dimen’ method that gets resolved for different screen densities and screen sizes.

densityDPI = density dots per inch of android device gotten from the display metrics of the device.

DENSITY_DEFAULT = constant from DisplayMetrics.

dimension = actual value the pixel value given to the formula will resolve into after calculation for different screen densities and screen sizes. This value is assigned to any space between two points in a component or space between two components which include length, width, height, breadth and (left, top, right and bottom of padding and margin) of components.

Note: You do not need to care about this formula or the ‘dimen’ method if you are using this library because all the works you will need to do with the method have already been done for you in the library. It’s only described here as the core of the library.

ADDING COMPONENT TO ANDROID PROJECT

Using Gradle;

Add the repository below to repositories block in your build.gradle (Project: <Project Name>) file:

allprojects {
        repositories {
        …
        maven {url ‘https://jitpack.io’}
        }
}

Add the dependency below to dependencies block in your build.gradle (Module: app) file:

dependencies {
        implementation ‘com.github.chibuzoio:component:1.0.1’
}

Click on ‘Sync Now’ or go to File and click on ‘Sync Project With Gradle Files’. The library will be added automatically into your project.

USING COMPONENT LIBRARY

Using the LoginActivity below for illustration:

The code below is responsible for the arrangement of the Activity above:

AU.disableDefaultActionBar(this);

VerticalLinearLayout activityContainer =
        new VerticalLinearLayout(this, GenericLayoutParams.MATCH_PARENT, GenericLayoutParams.MATCH_PARENT);
activityContainer.setComponentColor(R.color.whiteColor);

setContentView(activityContainer);

ScrollViewComponent scrollViewComponent =
        new ScrollViewComponent(activityContainer);

VerticalLinearLayout mainLayoutContainer =
        new VerticalLinearLayout(this, scrollViewComponent,
        GenericLayoutParams.MATCH_PARENT,
        GenericLayoutParams.MATCH_PARENT);
mainLayoutContainer.setLayoutGravity(Gravity.CENTER);
mainLayoutContainer.setGravity(Gravity.CENTER);

ImageViewComponent companyLogo =
        new ImageViewComponent(mainLayoutContainer, R.drawable.ymcmart);
companyLogo.setCircularCenterImage(R.drawable.ymcmart);
companyLogo.setImageSize(77.777f);

BorderlessEditText usernameEditText =
        new BorderlessEditText(mainLayoutContainer,
        R.drawable.icon_user, "Username");
usernameEditText.setMargins(23, 55.555f, 23, 0);

BorderlessEditText passwordEditText =
        new BorderlessEditText(mainLayoutContainer,
        R.drawable.icon_password, "Password");
passwordEditText.getBorderlessEditTextView()
        .setEditorInputType(EditTextComponent.INPUT_TYPE_TEXT_PASSWORD);
passwordEditText.setMargins(23, 11.111f, 23, 0);

ButtonComponent loginButton =
        new ButtonComponent(mainLayoutContainer, "Sign In");
loginButton.setMargins(23, 33.333f, 23, 23);

ButtonComponent signUpButton =
        new ButtonComponent(mainLayoutContainer, "Sign Up");
signUpButton.setDrawable(AU.curveBackgroundCorner(this, 11.111f, R.color.colorPrimaryDarker));
signUpButton.setMargins(23, 0, 23, 0);

TextViewComponent forgotPasswordTextLink =
        new TextViewComponent(mainLayoutContainer, "Forgot Password?", 5);
forgotPasswordTextLink.setMargins(23, 15.333f, 23, 33.333f);
forgotPasswordTextLink.setAlignment(TextViewComponent.TEXT_ALIGN_RIGHT);
forgotPasswordTextLink.setTextStyle(TextViewComponent.BOLD_TEXT);
forgotPasswordTextLink.setTextViewColor(R.color.genericLink);

The code snippet above was written in the onCreate method of LoginActivity, but can be isolated as a private method of the activity and called in the onCreate method. Description of the code snippet is as below:

disableDefaultActionBar of AU (Activity Utility) class removes the activity’s default ActionBar.

activityContainer is the base component that holds all the components of LoginActivity in place. That’s why it’s set to render all other components of the LoginActivity by setContentView method of LoginActivity. The constructor of activityContainer object contains two other parameters which are constants of GenericLayoutParams class. (Note: Always choose layout params constants (WRAP_CONTENT and MATCH_PARENT) from GenericLayoutParams and not from the LayoutParams class if you are using this library).

Note: Every component takes layout component (like FrameLayout, VerticalLinearLayout, HorizontalLinearLayout, ScrollView and so on) as one of its parameters because the layout component holds the component in position except the first (or base) layout component that is set for the activity by the setContentView method of the activity.

GenericLayoutParams class takes care of layout management of components. You do not have to concern yourself with what is happening in this class if you are only using the library, unless you are contributing to the development of the library.

scrollViewComponent takes care of scrolling should in case the the components of the LoginActivity grows past the screen size.

scrollViewComponent by convention can only contain one component. So, mainLayoutContainer is the only component contained by scrollViewComponent and it forms the base container for all other components contained by LoginActivity.

Note: Instead of setting orientation off from LinearLayout class, the LinearLayout got divided into two types of LinearLayout; HorizontalLinearLayout and VerticalLinearLayout.

Setting gravity and layout gravity using this library has been simplified into a single method call. E.g:

mainLayoutContainer.setGravity(Gravity.CENTER);
mainLayoutContainer.setLayoutGravity(Gravity.CENTER);

The two method calls above for setting gravity and layout gravity respectively are responsible for aligning the mainLayoutContainer which contains other components to the center of the scrollViewComponent.

From the mainLayoutContainer going down, the trend (the simplicity involved in creating UI components) continues downward because the design goal of Component library is that every component should be designed as a single entity (as one class) throughout the entirety of the project and have its object created and used where ever it’s needed. Complex components are created by composing other simple or complex components into one component. Some examples of simple components in this library include: DrawerLayoutComponent, FrameLayoutComponent, ViewPagerComponent, EditTextComponent, ScrollViewComponent, TextViewComponent, and ViewComponent. These components are termed simple components because they inherit directly from the known Android UI classes which respectively are: DrawerLayout, FrameLayout, ViewPager, AppCompatEditText, ScrollView, AppCompatTextView and View. On the other hand, some examples of complex components include: HorizontalLinearComponent, VerticalLinearComponent, BorderlessEditText, ButtonComponent and FormFieldComponent. The first two complex components inherit directly from LinearLayoutComponent, while the last three inherit from VerticalLinearComponent. These complex components are also composed of other simple or complex components.

GenericLayoutParams Class

This class controls the arrangement of components horizontally and vertically relative to their parent layouts and contents.

Private Fields
ViewGroup.LayoutParams layoutParams

Constants
public static final int ZERO_SPACE
public static final int MATCH_PARENT
public static final int WRAP_CONTENT

As their names imply, ZERO_SPACE gives zero as the width or height of layout, MATCH_PARENT gives the width or height of layout the exact width or height of its parent layout, while WRAP_CONTENT gives the width or height of layout the exact width or height that will suitably wrap its contents.

Public Constructors
GenericLayoutParams(ViewGroup viewGroup, int horizontalParam, int verticalParam)

GenericLayoutParams constructor takes ViewGroup or an object of any class that extends ViewGroup directly or indirectly as its first parameter. The second and third parameters are any of the constants of GenericLayoutParams class (ZERO_SPACE, MATCH_PARENT or WRAP_CONTENT).

Public Methods
void setLayoutMargin(View view, float left, float top, float right, float bottom)
void setLayoutGravity(View view, int gravity)
ViewGroup.LayoutParams getLayoutParams()

All the methods of GenericLayoutParams class alter layout dimensions (parameters) of all the Views (components) given to them except getLayoutParams method, which returns the layout parameters.

Packages of need in Component library include:
- layoutcomponent
- viewcomponent
- utility

layoutcomponent package contains the layout component classes in this library which include:
- DrawerLayoutComponent
- FrameLayoutComponent
- HorizontalLayoutComponent
- LinearLayoutComponent
- RecyclerViewComponent
- RelativeLayoutComponent
- VerticalLinearLayout
- ViewPagerComponent

viewcomponent package contains the view component classes in this library which include:
- BorderlessEditText
- ButtonComponent
- EditTextComponent
- FormFieldComponent
- IconLabelButton
- IconOnlyButton
- IconTextMenuComponent
- ImageViewComponent
- ImageViewParent
- ImageViewScreen
- ProgressBarComponent
- RoundElevatedPicture
- ScrollViewComponent
- SlideMenuComponent
- TextViewComponent
- ViewComponent

utility package contains the utility class which is:
AU (short for Activity Utility)

Starting with the classes in the layoutcomponent package;

DrawerLayoutComponent Class

This is a layout component that allows components to be pulled out from left edge, right edge or left and right edges of the window.

DrawerLayoutComponent inherits from androidx.drawerlayout.DrawerLayout